FICHE  META_INFORMATION_PARAMETRES

(à remplir par le responsable du paramètre)

### Nom du DATASET / Data SET NAME

Data set Name (list of the measured parameters):  POC biodegradation/photo-oxidation/autoxidation

PROJET-ETUDE / PROJECT TITLE

Campaign  NAME :   GreenEdge – AMUNDSEN – 2016	LEG :  1b

Date begin : June 23rd, 2017

Date end :  July 14th, 2017

Chief Scientist: Marcel Babin / Jean-Eric Tremblay

Address :

Université Laval - UMI Takuvik

1045 avenue de la médecine

Québec, QC, G1V0A6, Canada

OPERATION (if Relevant)

Sampling method:  Filtration on GFF (nominal porosity 0.7 µm)

Station number-Cast number:  Every full station

Operation code :

### RESPONSABLE SCIENTIFIQUE du paramètre / PI of the parameter

### DATASET contact

### INFORMATION GEOGRAPHIQUES /  GEOGRAPHIC INFORMATION

Predefined site (if relevant):

Location: Baffin Bay

LATITUDE: 59 – 73N

LONGITUDE  55 – 65W

### DESCRIPTION DES INSTRUMENTS / INSTRUMENTS DESCRIPTION (if Relevant)

Instrument Type: GC-MS

Manufacturer:  Agilent

Model: 7890B/7200 GC/QTOF System

Instrument Features / Calibration: A cross-linked 5% phenyl-methylpolysiloxane (Agilent; HP-5MS ultra inert) (30 m ( 0.25 mm, 0.25 m film thickness) capillary column was employed. Analyses were performed with an injector operating in pulsed splitless mode set at 270°C and the oven temperature programmed from 70°C to 130°C at 20°C min-1 and then to 300°C at 5°C min-1. The pressure of the carrier gas (He) was maintained at 0.69 ( 105 Pa until the end of the temperature program. Instrument temperatures were 300°C for transfer line and 230°C for the ion source. Accurate mass spectra were recorded across the range m/z 50-700 at 4 GHz. The QTOF-MS instrument provided a typical resolution ranging from 8009 to 12252 from m/z 68.9955 to 501.9706. Perfluorotributylamine (PFTBA) was utilized for daily MS calibration.

### DESCRIPTION DES PARAMETRES /  PARAMETERS DESCRIPTION

# Ce qui a été collecté, mesuré et comment / How was the parameter collected and measured (include references for analytical methods)?

Sampling: Samples were filtered through pre-weighed Whatman glass fiber filters (porosity 0.7 µm, diameter 25 or 47 mm, combusted 4 h at 450°C) and kept frozen at -20°C prior to analysis.

Analytical procedure: (briefly, could be a short recall to a published reference): As analyzed in Petit et al., 2015.

Units: gramme

Sensor Precision: Pico

# Décrire quels types de données sont nécessaires pour vous compléter votre propre jeu de données avant envoi à la base de données, et estimer le délai avant la disponibilité de vos données pour la base de données / Post-cruise data analysis/treatment required, and the time frame for this

Estimated Date of Delivery : End of 2018

### REFERENCES BIBLIOGRAPHIQUES

Petit, M., Bonin, P., Amiraux, R., Michotey, V., Guasco, S., Armitano, J., Jourlin-Castelli, C., Vaultier, F., Méjean, V., Rontani, J.-F., 2015. Dynamic of bacterial communities attached to lightened phytodetritus. Environ Sci Pollut Res Int 22, 13681–13692. doi:10.1007/s11356-015-4209-0

# Text boxes

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Rontani JF | 163 av. de luminy, 13288 Marseille | +33486090602 |  | jean-francois.rontani@mio.osupytheas.fr |

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Amiraux R | 163 av. de luminy, 13288 Marseille | +33486090521 |  | remi.amiraux@mio.osupytheas.fr |