FICHE  META_INFORMATION_PARAMETRES

(à remplir par le responsable du paramètre)

### Nom du DATASET / Data SET NAME

Data set Name (list of the measured parameters): endobenthos biodiversity

- diversity

- abundance

- biomass

- sediment grain-size

- sediment pigment content

- sediment organic carbon content

### PROJET-ETUDE / PROJECT TITLE

Campaign  NAME :   	GreenEdge – Amundsen – 2015	LEG : 4

Date begin : 2015-10-01

Date end : 2015-11-01

Chief Scientist: Philippe Archambault

Address :

Institut des sciences de la mer, Université du Québec à Rimouski

310 allée des Ursulines

Rimouski, Québec, G5L 3A1

### OPERATION (if Relevant)

Sampling method : benthos sampling using a box corer (0.25 m2), 20-30 cm depth

Station number-Cast number :  station 177

Operation code :

### RESPONSABLE SCIENTIFIQUE du paramètre / PI of the parameter

### DATASET contact

### INFORMATION GEOGRAPHIQUES /  GEOGRAPHIC INFORMATION

Predefined site (if relevant):

Location: station 177, Qikiqtarjuag

LATITUDE: 67°28.430

LONGITUDE: 63°41.526

### DESCRIPTION DES INSTRUMENTS /  INSTRUMENTS DESCRIPTION (if Relevant)

Instrument Type: precision box corer

Manufacturer: McGregor GeoScience Limited

Model:

Instrument Features / Calibration:

### DESCRIPTION DES PARAMETRES /  PARAMETERS DESCRIPTION

# Ce qui a été collecté, mesuré et comment / How was the parameter collected and measured (include references for analytical methods)?

Sampling: The box corer was deployed to quantitatively sample diversity, abundance and biomass of endobenthic fauna and to obtain sediment cores for sediment analyses. Sediments of usually a surface area of 0.125 m2 and 10-15 cm in depth were collected and passed through a 0.5 mm mesh sieve and preserved in a 4 % formaldehyde solution for further identification in the laboratory. Sub-cores of sediments were collected for sediment pigment content, organic carbon content, and sediment grain size; for sediment pigments and organic carbon content, the top 1 cm was collected, although for sediment grain size, the top 5 cm was collected. Sediment pigment samples were frozen at -80°C, and organic carbon samples and sediment grain size samples were frozen at -20°C. All samples have been transported off the ship for analyses in the lab at the Université du Québec à Rimouski.

Analytical procedure : (briefly, could be a short recall to a published reference):

Units:

Sensor Precision:

# Décrire quels types de données sont nécessaires pour vous compléter votre propre jeu de données avant envoi à la base de données, et estimer le délai avant la disponibilité de vos données pour la base de données / Post-cruise data analysis/treatment required, and the time frame for this

Estimated Date of Delivery :

### REFERENCES BIBLIOGRAPHIQUES

# Text boxes

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Philippe Archambault | 310 allée des Ursulines Rimouski, Qc, G5L 3A1 | 418-723-1986 poste 1765 | 418-724-1842 | philippe_archambault@uqar.ca |

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Philippe Archambault | 310 allée des Ursulines Rimouski, Qc, G5L 3A1 | 418-723-1986 poste 1765 | 418-724-1842 | philippe_archambault@uqar.ca |