FICHE  META_INFORMATION_PARAMETRES

(à remplir par le responsable du paramètre)

### Nom du DATASET / Data SET NAME

CTD sampling

### PROJET-ETUDE / PROJECT TITLE

Campaign  NAME :   	GreenEdge – ICECAMP – 2015	LEG : 1,2,3,4

Date begin : 28 mars 2015

Date end : 14 juillet 2015

Chief Scientist: Marcel Babin

Address :

Université Laval

UMI Takuvik

1045 avenue de la médecine

Québec, QC, G1V0A6, Canada

### OPERATION (if Relevant)

La CTD était couplée à l’UVP (underwater video profiler). Le protocole de déploiement suivi pendant les opérations GreenEdge15 était comme suit:

1) CTD-on en surface

2) Descente (min 0.3m/sec) à 10 dbar, temps d’attente >60s pour démarrage de la caméra-UVP

3) Decente à 22 dbar (démarrage système UVP >15m)

4) La couple remonte à 0 dbar pour commencer le profil

5) Descente à 350 dbar

6) Ascente (min .3m/sec)

### RESPONSABLE SCIENTIFIQUE du paramètre / PI of the parameter

### DATASET contact

### INFORMATION GEOGRAPHIQUES /  GEOGRAPHIC INFORMATION

Predefined site (if relevant):

Location: Camp de glace, Polarhaven- trou principal

LATITUDE:  67.4796N

LONGITUDE -63.7900 W

### DESCRIPTION DES INSTRUMENTS /  INSTRUMENTS DESCRIPTION (if Relevant)

Instrument Type:  CTD

Manufacturer: Seabird

Model:  SBE9+ V2

Instrument Features / Calibration: Calibrated on early 2015, previous to ice camp activities.

### DESCRIPTION DES PARAMETRES /  PARAMETERS DESCRIPTION

# Ce qui a été collecté, mesuré et comment / How was the parameter collected and measured (include references for analytical methods)?

Conductivity

Range: 0 to 9 S/m

Initial accuracy: +- 0.0005 S/m

Typical stability: 0.0003 S/m per month

Resolution: 0.00005 S/m typical

Temperature

Range: -5 to +35 degrees celsius

Initial accuracy: +- 0.005 deg. celsius

Typical stability: 0.0002 deg. celsius per month

Resolution: 0.0001 deg. celsius

Pressure

Range: Strain gauge 0 to 20 / 100 / 350 / 600 / 1000 / 2000/ 3500 / 7000 m;

Quartz 0 to  20 / 60 / 130 / 200 / 270 / 680 / 1400 / 2000 / 4200 / 7000 / 	10,500 m

Initial accuracy: Strain gauge ± 0.1% of full scale range; Quartz± 0.02% of full scale range

Typical stability: Strain gauge 0.1% of full scale range per year; Quartz 0.02% of full scale range per year

Resolution: Strain gauge 0.002% of full scale range; Quartz 0.0025% of full scale range

### REFERENCES BIBLIOGRAPHIQUES

Seabird :

http://www.seabird.com/sbe19plusv2-seacat-ctd

# Text boxes

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Responsable:Claudie Marec |  |  |  | Claudie.Marec@takuvik.ulaval.ca |
| Contact: José Lagunas | Ulaval-Takuvik Local 2052 | 418 656-2131, poste 7495 | 418 656-2339 | jose-luis.lagunas@takuvik.ulaval.ca |

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Pascal Guillot | UQAR-ISMER Local : O-118 | 418 723-1986 poste 1896 |  | pascal_guillot@uqar.ca |