FICHE  META_INFORMATION_PARAMETRES

(à remplir par le responsable du paramètre)

### Nom du DATASET / Data SET NAME

### PROJET-ETUDE / PROJECT TITLE

Campaign  NAME :   	GreenEdge – ICECAMP – 2015	LEG : 2,3,4

Date begin : 16/04/2015

Date end : 10/7/2015

Chief Scientist: Marcel Babin

Address :

Université Laval

UMI Takuvik

1045 avenue de la médecine

Québec, QC, G1V0A6, Canada

### OPERATION (if Relevant)

A 300KHz Teledyne RDI Workhorse Sentinel ADCP was deployed ice-mounted and downward looking through a 10inch auger hole in coordinates 67°28.774N 63°46.398W for sampling a water depth of 100m.

### RESPONSABLE SCIENTIFIQUE du paramètre / PI of the parameter

### DATASET contact

### INFORMATION GEOGRAPHIQUES /  GEOGRAPHIC INFORMATION

Predefined site (if relevant):

Location: Ice, snow, seawater, melt pond, atmosphere

LATITUDE:  67°28.774N

LONGITUDE 63°46.398W

### DESCRIPTION DES INSTRUMENTS /  INSTRUMENTS DESCRIPTION (if Relevant)

Instrument Type:  ADCP

Manufacturer: Teledyne RD

Model:   Workhorse Sentinel 300 KHz

Instrument Features / Calibration: Calibrated on site

### DESCRIPTION DES PARAMETRES /  PARAMETERS DESCRIPTION

# Ce qui a été collecté, mesuré et comment / How was the parameter collected and measured (include references for analytical methods)?

Sampling: Acoustic sampling, see Operation section.

Analytical procedure : (briefly, could be a short recall to a published reference):

Units:

Sensor Precision:

Velocity accuracy: 0.5% of the water velocity reative to ADCP +- 0.5 cm/s

Velocity resolution: 0.1 cm/s

Velocity range: +- 5 m/s (default) +- m/s (max)

Number of depth cells: 1-255

Pingrate: Upt to 10 Hz

Depth cell size: Typical depth 110 m

Vertical resolution: 1m –> range=83m and std. Dev.= 14 cm/s

Vertical resolution: 2m –> range=93m and std. Dev.= 7 cm/s

Vertical resolution: 4m –> range=103m and std. Dev.= 3.6 cm/s

Vertical resolution: 8m –> range=116m and std. Dev.= 1.8 cm/s

Precision:

Temperature (mounted on transducer) Range -5° to 45°C, Precision ±0.4°C, Resolution 0.01°

Tilt Range ±15°, Accuracy ±0.5°, Precision ±0.5°, Resolution 0.01°

Compass (fluxgate type, includes built-in field calibration feature) Accuracy ±2°5, Precision ±0.5°5,

Resolution 0.01°, Maximum tilt ±15°. Compass was calibrated on-site.

# Décrire quels types de données sont nécessaires pour vous compléter votre propre jeu de données avant envoi à la base de données, et estimer le délai avant la disponibilité de vos données pour la base de données / Post-cruise data analysis/treatment required, and the time frame for this

Estimated Date of Delivery :

### REFERENCES BIBLIOGRAPHIQUES

Teledyne RD :

http://rdinstruments.com/__documents/Brochures/sentinel_datasheet_lr.pdf

# Text boxes

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Responsable:Claudie Marec |  |  |  | Claudie.Marec@takuvik.ulaval.ca |
| Contact: José Lagunas | Ulaval-Takuvik Local 2052 | 418 656-2131, poste 7495 | 418 656-2339 | jose-luis.lagunas@takuvik.ulaval.ca |

| Nom / name | adresse / address | téléphone / phone number | fax / fax number | adresse mél / email address |
| --- | --- | --- | --- | --- |
| Marie Noelle Houssais |  |  |  |  |